## Slide 1: WES 237B: Master of Advanced Study in Wireless Embedded Systems
Pat Pannuto
Department of Computer Science and Engineering
University of California, San Diego
Summer Session 2022

## Slide 2: WELCOME to WES 237B!

## Slide 3: Designing and Optimizing Embedded Systems (Signal/Image/Video Processing) Applications on SoC

## Slide 4: Designing and Optimizing Embedded Systems (Signal/Image/Video Processing) Applications on SoC

## Slide 5: What is an embedded system?

## Slide 6: What is an embedded system?
Specialized
Low power
Real-time
Properties of embedded systems

## Slide 7: What is an embedded system?
Specialized
Low power
Real-time
High-performance
Properties of embedded systems

## Slide 8: What is an embedded system?
A domain-specific + high-performance system

## Slide 9: What is an embedded system?
A domain-specific + high-performance system
Achieving high-performance while reducing power consumption is a key, and how to do that?
There is no single answer! Usually, involves multiple factors (tradeoff) latency, throughput, power, cost,...

## Slide 10: What is an embedded system?
A domain-specific + high-performance system
Achieving high-performance while reducing power consumption is a key, and how to do that?
There is no single answer! Usually, involves multiple factors (tradeoff) latency, throughput, power, cost,... What is ”performance” anyway??

## Slide 11: How to design an embedded system for this app?
void matrix_vector_multiply(int in1[SIZE][SIZE], int in2[SIZE], int out[SIZE]) {
for(int i = 0; i < SIZE; i++){
for(int j = 0; j < SIZE; j++){
acc = acc + in1[i][j] * in2[j];
}
out[i] = acc;
}
}
void prefix_sum(int in[SIZE], int out[SIZE]) {
for(int i = 1; i < SIZE; ++i){
out[i] = out[i-1] + in[i];
}
}
int main() {
matrix_vector_multiply(A, B, C);
prefix_sum(C, D);
return 0;
}
0
2
1
6
3
1
2
5
0
2
3
9
12
13
15
20
Notes: Work through what each function actually computes
- show trivial to //ize MVMultiply (vectorize/unroll inner loop)
- why harder to //ize prefix sum (w/ naïve impl. at least)

## Slide 12: Embedded systems design  Trade-offs
Performance, power, cost, programming choice,…etc.
Matrix Vector Multiplication
Prefix sum
CPU

## Slide 13: Embedded systems design  Trade-offs
Performance, power, cost, programming choice,…etc.
Matrix Vector Multiplication
Prefix sum
Parallel
Sequential
FPGA + CPU

## Slide 14: Embedded systems design  Trade-offs
Performance, power, cost, programming choice,…etc.
Matrix Vector Multiplication
Prefix sum
Parallel
Sequential
FPGA + CPU
What if memory is bottleneck?

## Slide 15: Embedded systems design  Trade-offs
Performance, power, cost, programming choice,…etc.
Matrix Vector Multiplication
Prefix sum
Parallel
Sequential
GPU ?

## Slide 16: Embedded systems design  Trade-offs
Performance, power, cost, programming choice,…etc.
Matrix Vector Multiplication
Prefix sum
Parallel
Sequential
GPU ?
Can you re-write the Prefix sum (seq code) to tailor parallel architecture?

## Slide 17: Designing and Optimizing Embedded Systems (Signal/Image/Video Processing) Applications on SoC

## Slide 18: Why study signal/image/video processing?
Emerging applications ADAS/AR/VR uses vision/image processing
Requires high performance and low power

## Slide 19: Why study signal/image/video processing?
Emerging applications ADAS/AR/VR uses vision/image processing
Requires high performance and low power

## Slide 20: Designing and Optimizing Embedded Systems (Signal/Image/Video Processing) Applications on SoC

## Slide 21: What is a System-on-chip (SoC)?

## Slide 22: System on a Chip (SoC)
The Zynq Book http://www.zynqbook.com/

## Slide 23: System on a Chip (SoC)
The Zynq Book http://www.zynqbook.com/, http://www.pynq.io/

## Slide 24: SoC
UART
DSP
Memory Controller
DMA
USB
ADC/DAC
CPU
Softcore
Notes: Large number of modules
Special function
Your system is s
How are you going to connect these modules ?
What happens if I add new IP
We need a standard.

## Slide 25: SoC
UART
DSP
Memory Controller
DMA
USB
ADC/DAC
Softcore
CPU
Notes: Ask folks to find the CPU in the block diagram 

## Slide 26: SoC
UART
DSP
Memory Controller
DMA
USB
ADC/DAC
Softcore
CPU

## Slide 27: SoC
UART
DSP
Memory Controller
DMA
USB
ADC/DAC
Softcore
CPU
Vendors buy ARM IP Cores and develop SoCs
  Xilinx Zynq/Pynq
  Jetson Nvidia
A protocol
  Must be standard
  Maintenance
  Modularity (Re-use)

## Slide 28: SoC
UART
DSP
Memory Controller
DMA
USB
ADC/DAC
Softcore
CPU
Different protocols…
Core-Connect (IBM)
Wishbone (OpenCores/OSH)
AXI  ARM’s
  Xilinx bought in most here
Avalon (Altera, now Intel)
MIPI… [~mobile phones]
  SLIMBus, LLI, UniPro, I3C, …

## Slide 29: SoC
CPU
Co-processor
Peripherals

## Slide 30: SoC
CPU/GPU
Co-processor (Accelerator Design)
Peripherals
WES 237B
WES 237C

## Slide 31: ARM
Introduced in 1980s into customer electronics
De facto embedded processor technology
  Not usually manufactured as a standalone chip
  Usually part of a System-on-chip that is customized for specific application
ARM is everywhere including your phone, TV, ipad,… as a form of SoC.
SoC is a collection of interconnected hardware modules
A typical SoC include one or more ARM processor cores
First major customer was Apple (Netwon PDA)

## Slide 32: Apple A8 (iPhone 6) … Apple A15 (iPhone 13)

## Slide 33: ARM Technology
ARM (Advanced RISC Machine) controlled by ARM
ARM writes specification of ARM processors
Specifications
  Instruction set architecture
  MMU
  Interrupt and Exception handling
  Caches
  Virtualization
CPUs based on ARM1, ARM2, ARM3 instruction set architecture (ISA) were introduced around 1980s.
Due to computations from Intel x86 and Motorola 68,000 CPU, ARM switched its business model
  Selling the rights to use its processor design or ISA (specification)
ARMv4, ARMv5, ARMv6, ARMv7, ARMv8

## Slide 34: ARM Technology
ARM holding creates IP cores based on specifications
IP core = VHDL or Verilog implementation of a specification
Examples:
  ARM976 = Implementation of ARMv5
  ARM1176 = Implementation of ARMv6
  Cortex – A15 = Implementation of ARMv7-A
  Cortex- A53 = Implementation of ARMv8-A
Multiple implementation of the same specification is possible
  Cortex-A5,6,7,…15
  Cortex-A5 is low power, Cortex-A15 is high-performance
  Difference of pipeline, out of order execution, size of cache, ,…

## Slide 35: ARM Processor Families
Three ‘profiles’ of cores:
  Cortex-A Application
  Cortex-R Real Time
  Cortex-M Mobile
… get it?

## Slide 36: ARM Technology
ARM processors are sold as a reusable IP cores
Consistent instruction set allows
  Common tool chain such as compilers debuggers, and code libraries
Most ARM processors are used with Co-processors (FPGA, GPU,..)

## Slide 37: ARM Technology
Specification
e.g., ARMv7
ARM IP core
Cortex-A9
SoC
e.g., Zynq
Hardware Platform
e.g., Pynq, Zedboard

## Slide 38: WES237B Hardware
  Open source project to use Xilinx platforms
  Xilinx Zynq Chip
  PL & PS part
  Allows to use python/libraries to program PS/PL
Tegra K1 SOC
  NVIDIA Kepler GPU with 192 CUDA Cores
  NVIDIA 4-Plus-1™ Quad-Core ARM® Cortex™-A15 CPU
2 GB x16 Memory with 64-bit Width
http://www.nvidia.com/object/jetson-tk1-embedded-dev-kit.html

## Slide 39: WES 237B
Course web:
  https://patpannuto.com/classes/2022/summer/wes237b
Instructor
  10-year anniversary of embedded systems work
  Primary research thrusts on ‘more embedded’ applications
Amazing TA
  Teaching experience across many courses and significant experience with embedded platforms
  Technically very strong – your hands-on expert!

## Slide 40: What to expect from WES 237B?
Goal 1: Optimization/Performance measurement of emerging applications on a SoC
  Software optimization for SoC (pipelining, unrolling, multi-threading), blocking, memory optimizations
Goal 2: Understanding Parallel Programming Paradigms and Parallel Patterns
  Understanding parallel programming using emerging applications (covers some case studies using computer vision/image processing applications)

## Slide 41: Grading and Grading Policy
Grading
  Student group research and participation: 30%
    Class participation 10%
    Group research and presentation 20%
  Assignments : 70%
    Assignment 1: 10%
    Assignment 2 to 5 : 15%
  Assignments are for groups of 2
  Group presentations are for different group of 2 — network! 
  No show up/being late: -5% from your grade (need to get explicitly permission) each occasion (preferably in advance, but life happens)

## Slide 42: Group Research Presentation (~50 minutes)
Content: How well your presentation covers the given topic (specific materials/papers will be given)?5%
Presentation: How you are presenting the material to audience of a wide background in an allocated time? 5%
Discussion and Future Directions /Questions: Leading the discussion (discussing pros/cons) of the technology including benefits, current technological challenges/limitations and opportunities, how this work is different than previous ones (what are the main contributions)?10%
  Instructors/TAs/students will ask questions & participate in the discussion
Logistics
  Send me the outline of your presentation at least a week before the class
  Discuss/send me the (close to final) presentation 2 days before the class.

## Slide 43: Student Group Presentation Topics (Tentative)
Emerging Memory Technologies & in-memory computing
  https://emai19.sites.stanford.edu/workshop-presentations
  Phase Change Memory
Emerging Processing Technologies
  Optical computing https://lighton.ai/, https://lightmatter.co/, https://www.optalysys.com/
Efficient Deep Learning Hardware/Software Architectures
  Sze, Vivienne, et al. "Hardware for machine learning: Challenges and opportunities." 2017 IEEE Custom Integrated Circuits Conference (CICC). IEEE, 2017. https://arxiv.org/pdf/1612.07625.pdf
  https://cs217.stanford.edu/
  Han, Song, et al. "EIE: efficient inference engine on compressed deep neural network." ACM SIGARCH Computer Architecture News 44.3 (2016): 243-254. https://arxiv.org/pdf/1602.01528.pdf
  Gamboa, Noah, et al. "Campfire: Compressible, Regularization-Free, Structured Sparse Training for Hardware Accelerators." arXiv preprint arXiv:2001.03253 (2020) https://arxiv.org/pdf/2001.03253.pdf
  Yao, Shuocaho, et al. “DeepIoT: Compressing Deep Neural Network Structures for Sensing Systems with a Compressor-Critic Framework.” https://dl.acm.org/doi/abs/10.1145/3131672.3131675
Emerging Parallel Programming Systems of Parallel Architectures
  Lai, Yi-Hsiang, et al. "HeteroCL: A multi-paradigm programming infrastructure for software-defined reconfigurable computing." Proceedings of the 2019 ACM/SIGDA International Symposium on Field-Programmable Gate Arrays. 2019.
  Li, Tzu-Mao, et al. "Differentiable programming for image processing and deep learning in Halide." ACM Transactions on Graphics (TOG) 37.4 (2018): 1-13.
Emerging Sensor Technologies and Enabling Applications
  Dynamic Vision Sensor
    http://rpg.ifi.uzh.ch/CVPR19_event_vision_workshop.html
  Processing inside the sensor
    Sony IMX 500 https://www.cinema5d.com/sony-imx500-worlds-ai-image-sensor-announced/

## Slide 44: WES 237B does not teach you C!
We do not teach you basics of C!
  Although, we cover advanced concepts and optimizations
We will try to help you
You are expected to catch up if you do not have C programming background
  Assignment 1 (part two) is about C programming

## Slide 45: Questions ?

## Slide 46: Embedded Compute and Text Compression

## Slide 47: Processors
ISA
  A definition of instructions that a processor can execute
  x86 is an ISA, many realization of x86
  ARMv1, ARMv2,…ARMv7 are ISAs.
Realization or Chip (“Soft” or “Hard” cores)
Software
Hardware
ISA
Notes: What are the advantages of sharing an ISA ?

## Slide 48: An Instruction Set Architecture is an abstraction of a computational machine
An ISA is “the agreed-upon interface between all the software that runs on the machine and the hardware that executes it.”
I/O system
Instr. Set Proc.
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Notes: the ISA is the HW/SW interface (book)
it is a useful abstraction in both directions.

## Slide 49: Computers do not speak English And they do not speak C or Java or Python or Haskell (or…) either
Compiler
High Level Language
(C, Java, Rust, etc)
Assembly Language
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
int temp = array[index];
array[index] = array[index + 1];
array[index + 1] = temp;
ALUOP[0:3] <= InstReg[9:11] & MASK
Machine Language
1000110001100010000000000000000
1000110011110010000000000000100
1010110011110010000000000000000
1010110001100010000000000000100
Control Signal Spec
Assembler
Machine Interpretation
Specification
Programmer
“Swap two array elements.”
Notes: imp points.
-the computer doesn’t understand for i=0ton
-one-to-many HLL to AL
-one-to-one AL to ML
-ISA (grey box) is fixed
a computer is a device you can give commands to. But only a very limited set of commands. That set is the IS. It is the language the computer understands.
But at a low level, it doesn’t even really understand that...
Abstraction.
Computer understands only ones and zeroes. But it also understands groups of ones and zeroes, so it understands larger numbers. That is useful abstraction for the computer.

## Slide 50: The Instruction Set Architecture
that part of the architecture that is visible to the programmer
  available instructions (“opcodes”)
  number and types of registers
  instruction formats
  storage access, addressing modes
  exceptional conditions
Notes: Note: visible to programmer includes by extension all the tools used by the programmer (i.e. toolchains)

## Slide 51: Embedded Compute Units
Processor | Description | Applications
Microcontroller | Microcontrollers is a small computer (CPU, memory I/O) | Suitable for application that require small memory and less computation
DSP | Processors specifically designed for signal processing Repetitive numeric computations High memory bandwidth (arrays) Real-time processing DSP objectives Power Development time Throughput (Processing) | Audio Coding/Decoding Video/Image/ Computer Vision Convolution Communications FIR, FFT
GPU | Graphics processors (GPGPU) | General (embedded  data center)
FPGA | Programmable Custom Hardware | General (embedded  data center)

## Slide 52: Design tradeoffs…
CPU
DSP
GPU
FPGA
ASIC
Efficiency, performance (given workload..)
Generality, flexibility

## Slide 53: A field-programmable gate array (FPGA)

## Slide 54: What is an FPGA?
A field-programmable gate array (FPGA)

## Slide 55: What is an FPGA?
A field-programmable gate array (FPGA)

## Slide 56: FPGA
Flexibility to implement any logic
  F(x,y,z) = xy + z’
  F(x,y,z) = xyz

## Slide 57: FPGA
Flexibility to implement any logic
  F(x,y,z) = xy + z’
  F(x,y,z) = xyz

## Slide 58: FPGA
Flexibility to implement any logic
  F(x,y,z) = xy + z’
  F(x,y,z) = xyz

## Slide 59: Why FPGAs?
A field-programmable gate array (FPGA)
Vision (image)  High performance and low (er) power

## Slide 60: Motivation: Applications of FPGA
Data centers[1]
[1] Andrew Putnam et al. “ A Reconfigurable Fabric for Accelerating Large-Scale Datacenter Services,”, ISCA, 2014
Notes: FPGAs are emerging as an alternative platofrm for a number of computationally depending applications due to its performance per watt benefits.

## Slide 61: Motivation: Applications of FPGA
Data centers[1]
Database[2]
[1] Andrew Putnam et al. “ A Reconfigurable Fabric for Accelerating Large-Scale Datacenter Services,”, ISCA, 2014
[2] Casper et al. "Hardware acceleration of database operations", FPGA''14
Notes: FPGAs are emerging as an alternative platofrm for a number of computationally depending applications due to its performance per watt benefits.

## Slide 62: Motivation: Applications of FPGA
Data centers[1]
Database[2]
CNN [3]
[4] Rouhani et al. "SSketch: An Automated Framework for Streaming Sketch-based Analysis of Big Data on FPGA.", FCCM 2015
[1] Andrew Putnam et al. “ A Reconfigurable Fabric for Accelerating Large-Scale Datacenter Services,”, ISCA, 2014
[2] Casper et al. "Hardware acceleration of database operations", FPGA''14
[3] Zhang et al. "Optimizing fpga-based accelerator design for deep convolutional neural networks.", FPGA 2015
Big Data[4]
Notes: FPGAs are emerging as an alternative platofrm for a number of computationally depending applications due to its performance per watt benefits.

## Slide 63: Motivation: Applications of FPGA
Data centers[1]
Database[2]
Big Data[4]
[4] Rouhani et al. "SSketch: An Automated Framework for Streaming Sketch-based Analysis of Big Data on FPGA.", FCCM 2015
[1] Andrew Putnam et al. “ A Reconfigurable Fabric for Accelerating Large-Scale Datacenter Services,”, ISCA, 2014
[2] Casper et al. "Hardware acceleration of database operations", FPGA''14
[3] Zhang et al. "Optimizing fpga-based accelerator design for deep convolutional neural networks.", FPGA 2015
CNN [3]
Notes: FPGAs are emerging as an alternative platofrm for a number of computationally depending applications due to its performance per watt benefits.

## Slide 64: Applications

## Slide 65: Designing an FPGA?
You will learn in WES 237C!

## Slide 66: Designing an FPGA ?
VHDL,

## Slide 67: Designing an FPGA?
VHDL,
Verilog,
SystemVerilog,
….

## Slide 68: VHDL???

## Slide 69: High-Level Synthesis: A way to program FPGA from C
C/C++
Magic
VHDL (Verilog)

## Slide 70: High-Level Synthesis
C/C++
Directives

## Slide 71: High-Level Synthesis
C/C++
Directives
HLS
Directives: Pipeline, partition, dataflow, inline,reshape, resource, stream, top, interface, expression balance, reset, allocation, dependence, function_initiate,…

## Slide 72: High-Level Synthesis
C/C++
Directives
VHDL (Verilog)
HLS
Directives: Pipeline, partition, dataflow, inline,reshape, resource, stream, top, interface, expression balance, reset, allocation, dependence, function_initiate,…

## Slide 73: High-Level Synthesis
C/C++
Directives
VHDL (Verilog)
HLS
void HelloWorld(
int A[8],
int B[8]) {
#pragma unroll
for(int i=0;i<8;i++){
B[i]=A[i]*3;
}
}

## Slide 74: High-Level Synthesis
C/C++
Directives
VHDL (Verilog)
HLS
void HelloWorld(
int A[8],
int B[8]) {
#pragma unroll
for(int i=0;i<8;i++){
B[i]=A[i]*3;
}
}

## Slide 75: High-Level Synthesis
C/C++
Directives
VHDL (Verilog)
Vivado HLS
Vivado
IP
Bitstream
void HelloWorld(
int A[8],
int B[8]) {
#pragma unroll
for(int i=0;i<8;i++){
B[i]=A[i]*3;
}
}

## Slide 76: Summary of Embedded Systems and Trends
Embedded systems  Getting complex
High performance computing & embedded systems  Merging
GPUs and FPGAs are two key players
  GPUs easy to program, high power consumption
    Good for bulk processing
  FPGAs hard(er) to program, low power consumption
    Good for streaming applications
    Flexibility
  ASIC Expensive and not flexible
    Power/performance
FPGA Moving towards SoC
  Programming from high-level languages such as C

## Slide 77: System on a Chip (SoC): Zynq
Processing System (PS)
  Application processor unit (APU)
  Memory interfaces
  I/O peripherals (IOP)
  Interconnect
Programmable Logic (PL)

## Slide 78: System on a Chip (SoC)
Lower cost
Faster and more secure data transfer between components
Smaller physical size
Lower power consumption
Has higher overall speed

## Slide 79: System on a Chip (SoC): Zynq

## Slide 80: PL Special Resources: BRAM & DSP48E1
Block Rams (BRAMs)
  RAM, ROM, FIFO
  Each block ram can store up to 36 Kb info
    Can be configured as 36Kb or 18Kb
DSP48E1
  Pre-adder/subtractor, multiplier, post-adder/subtractor
IOBs
  Pre-adder/subtractor, multiplier, post-adder/subtractor
XADC
  A dedicated set of ADC blocks
Clocks
  4 clocks from PS and other PL clocks

## Slide 81: PS an PL interface
Advanced eXtensible Interface (AXI)
  Version AXI4
  ARM AMBA® 3.0 open standard
  First release 1996 for microcontrollers
  De-facto standard for on-chip communication

## Slide 82: SoC Design Flow
Defining Requirements
Defining Specification
Software/ Hardware Partition
Software Development & Testing
Hardware Development & Testing
System Integration & Testing
Application

## Slide 83: Compression: Huffman Encoding

## Slide 84: Compression
Encoder
Decoder

## Slide 85: Huffman Encoding
Greedy Algorithm
Input: text data (symbols)
  Find histogram of symbols
  L = Sort according to frequencies (histogram) of symbols
  Create a Huffman tree
    Select two symbols with minimum frequencies
    Create a node and add their symbols
    Add the new node to L in a sorted order
  Assign a 0 to left edge and 1 to right edge
  Create a codeword from root of Huffman tree to the leaves of Huffman tree
  Return codeword

## Slide 86: Data Compression: Huffman Encoding
David Albert Huffman
  Invented during his PhD at MIT
“A Method for the Construction of Minimum-Redundancy Codes”, 1952
  Data: AAABB
Fixed Length Encoding:
    A = 001
    B= 010
     001001001010010  15 bits
Huffman Encoding:
  Variable Length Encoding
    A = 1
    B= 010
     111010010 9 bits

## Slide 87: Histogram
Input:
AABACDCDDDDEEEEEF

## Slide 88: Histogram
S | F
A | 3
B | 1
C | 2
D | 5
E | 5
F | 1
Input:
AABACDCDDDDEEEEEF

## Slide 89: Sorting by frequencies
Radix sort, merge sort, quick sort,…etc.
We will learn how to design parallel sorting algorithms

## Slide 90: Radix Sort
1 | 2 | 3
0 | 0 | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1
1 | 1 | 1
0 | 0 | 2
1 | 2 | 3
9 | 9 | 9
6 | 0 | 9
1 | 2 | 3
 |  | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1

## Slide 91: Radix Sort
1 | 2 | 3
0 | 0 | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1
1 | 1 | 1
0 | 0 | 2
1 | 2 | 3
9 | 9 | 9
6 | 0 | 9
6 | 0 | 9
0 | 0 | 2
1 | 1 | 1
1 | 2 | 3
9 | 9 | 9
1 | 2 | 3
 |  | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1

## Slide 92: Radix Sort
1 | 2 | 3
0 | 0 | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1
1 | 1 | 1
0 | 0 | 2
1 | 2 | 3
9 | 9 | 9
6 | 0 | 9
6 | 0 | 9
0 | 0 | 2
1 | 1 | 1
1 | 2 | 3
9 | 9 | 9
0 | 0 | 2
1 | 1 | 1
1 | 2 | 3
6 | 0 | 9
9 | 9 | 9
1 | 2 | 3
 |  | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1

## Slide 93: Radix Sort
Stage 1
Stage 2
Stage 3
1 | 1 | 1
0 | 0 | 2
1 | 2 | 3
9 | 9 | 9
6 | 0 | 9
6 | 0 | 9
0 | 0 | 2
1 | 1 | 1
1 | 2 | 3
9 | 9 | 9
0 | 0 | 2
1 | 1 | 1
1 | 2 | 3
6 | 0 | 9
9 | 9 | 9
Option 1: HW  pipeline
Option 2: Parallel Hardware
1 | 2 | 3
0 | 0 | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1
1 | 2 | 3
 |  | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1
Histogram
Prefixsum
H
P
H
Counting Sort
CS
CS
CS
Radix Sort
RS
RS
New Radix Sort
There are a number of ways of designing parallel algorithms.
Notes: Different stages of Radix sort is pipelined so that throughput of the overall system increases. Each stage of Radix sort is implemented by counting sort as shown by this algorithm. We explain the counting sort in next slide

## Slide 94: Counting Sort
[0, 3, 2, 2, 3, 2, 0, 3, 2, 1]
(C0, C1, C2, C3) = [2, 1, 4, 3]
(O0, O1, O2, O3) = (0, 2, 3, 7)
Calculate occurrence of each number. C0 is the count of 0
We take the prefix sum of the counts transforms it to an offset table.
[0, 0, 1, 2, 2, 2, 2, 3, 3, 3]
Input array
Re-order (copy out) step where values are
Copied into the right location using prefix table.
Counting sort/Radix sort are (parallel) architecture friendly algorithms
 Suitable for parallel architectures such as GPU (including multi core parallelization)

## Slide 95: Huffman Tree Creation
Create Tree
Sort
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
0
0
0
1
1
1
D
E
2
17
F
A
1
0
1
B
C
4
7
10
0

## Slide 96: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5

## Slide 97: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
B
1
n1
2
F
1

## Slide 98: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
n1 | 2
B
1
n1
2
F
1

## Slide 99: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
n1 | 2
B
1
n1
2
F
1

## Slide 100: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
n1 | 2
B
1
n1
2
F
1
n2
4
C
2

## Slide 101: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
n1 | 2
n2 | 4
B
1
n1
2
F
1
n2
4
C
2

## Slide 102: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
n1 | 2
n2 | 4
B
1
n1
2
F
1
n2
4
C
2
A
3

## Slide 103: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
n1 | 2
n2 | 4
n3 | 7
B
1
n1
2
F
1
n2
4
C
2
A
3
n3
7

## Slide 104: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
n1 | 2
n2 | 4
n3 | 7
n4 | 10
n5 | 17
B
1
n1
2
F
1
n2
4
C
2
n3
7
A
3
E
5
n4
10
D
5
n5
17

## Slide 105: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
Create Tree
Sort
B
1
n1
2
F
1
n2
4
C
2
n3
7
A
3
E
5
n4
10
D
5
n5
17

## Slide 106: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
Create Tree
Sort
B
1
n1
2
F
1
n2
4
C
2
n3
7
A
3
E
5
n4
10
D
5
n5
17
0
0
0
0
0
1
1
1
1

## Slide 107: Huffman Tree Creation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
Create Tree
Sort
B
1
n1
2
F
1
n2
4
C
2
n3
7
A
3
E
5
n4
10
D
5
n5
17
0
0
0
0
0
1
1
1
1
Symbol | Code
A | 00
F | 0100
B | 0101
C | 011
D | 10
E | 11
1
Huffman Tree Creation is Sequential Process
 Suitable for CPU architecture.

## Slide 108: Parallel Bit Length Calculation
S | F
F | 1
B | 1
C | 2
A | 3
D | 5
E | 5
Sort
Compute Bit Len
2
4
4
3
2
2
Create Tree
1 | 2 | 4 | 4 | 0
F | n1 | A | D | n3
B | C | n2 | E | n4
0 | 1 | 2 | 3 | 4
Parent Address
Left
Right
Address
This storage (Parent Address, Left, Right) allows parallel bit length calculation
Partitioning the Huffman Tree in horizontal direction at any point will result independent data in Parent Address, Left and Right
B
1
n1
2
F
1
n2
4
C
2
n3
7
A
3
E
5
n4
10
D
5
n5
17

## Slide 109: Text compression with Huffman Encoding
Encoder
Decoder
Encoder
Decoder
Bit
Length
Huffman Encoding
Canonical Huffman coding

## Slide 110: Canonical Huffman Encoding
Memory efficient
Faster decoding
Encoder
Decoder
Bit
Length
https://en.wikipedia.org/wiki/Canonical_Huffman_code

## Slide 111: Software Optimization

## Slide 112: Optimizations

## Slide 113: Optimize  Performance

## Slide 114: Measuring Performance
Notes: What are the goals of Software Optimization ?

## Slide 115: The bottom line: Performance
Time to do the task
  execution time, response time, latency
Tasks per day, hour, week, sec, ns. ..
  throughput, bandwidth
Ferrari
Bus
Speed
160 mph
65 mph
Time to Bay Area
3.1 hours
7.7 hours
Passengers
2
60
Throughput (pmph)
320
3900

## Slide 116: Measures of “Performance”
Execution Time
Throughput (operations/time)
  Transactions/sec, queries/day, etc.
Frame Rate
Responsiveness
Performance / Cost
Performance / Power
Performance / Energy
Different Metrics for different folks
ET is standard responsiveness
Frame Rate – FPS/Media App
Throughput (Servers)
Responsiveness – similar to ET but can vary, think ipod/smartphone
Perf/Cost – Server farm / everyone
Perf/Power – power is expensive and causes thermal issues(cooling)
Perf/Energy – battery-based designs

## Slide 117: Why Study Computer Performance?
In order to say X is n times faster than Y
Identify the benefits of running a program on a computer X, or bottlenecks of a program on a computer X
Embedded systems are too complex (CPU + FPGA + GPU)  How to measure performance of system consisting of sequential and parallel parts ?
To understand common techniques to measure performance
To know what to measure & how to measure

## Slide 118: Performance is Affected by,…

## Slide 119: Performance is Affected by,…
Technology
  Clock speed
  Processor technology

## Slide 120: Performance is Affected by,…
Technology
  Clock speed
  Processor technology
Organization
  Single core. vs. multi core
  Types of processors implementation (SIMD, out of order,..)
  Heterogeneous (SoC)
  Memory hierarchy & memory type
  Type of I/O devices
  ,…

## Slide 121: Performance is Affected by,…
Technology
  Clock speed
  Processor technology
Organization
  Single core. Vs. multi core
  Heterogeneous (SoC)
  Types of processors (SIMD, out of order,..)
  Memory hierarchy & memory type
  Type of I/O devices
  ,…
Software
  Quality of compilers & libraries & parallel processing frameworks
  Operating system

## Slide 122: Principles of Measuring Performance
Well defined metrics
  Execution time = Time spent running a program on X computer
Reproducibility
  Should get the same result when you are using the same program on same machine under same conditions (OS, compiler levels,…)
Standard Benchmarks
  SPEC (https://www.spec.org/benchmarks.html)

## Slide 123: Performance Metrics
Raw speed = peak performance
  In practice, never attainable
  Clock rate * #of floating point operations/cycle (E.g., 10 Gflops)
Execution time = time to execute a program from beginning to end
  The sooner the better
  Wall clock time/elapsed time: Time to complete task as seen by the user. Might include operating system overhead or interference with other applications
  CPU Time: does not include time spent for IO, external sources
    User CPU time: CPU time spent in the program
    System CPU time: CPU time spent in the OS performing taks requested by program
Throughput = total amount of work completed in a given time
  Frames per second (fps)., 30 fps
  Transactions or packets per second
  Indication of how well hardware resources are being used
Memory: Bandwidth & Latency

## Slide 124: There are many ways to measure program execution time
Program-reported time?
Wall-clock time?
user CPU time?
user + kernel CPU time?
$ time make # cargo build
Compiling hail v0.1.0 (/tock/boards/hail)
Finished release [optimized + debuginfo] target(s) in 19.96s
real 0m21.146s
user 0m30.388s
sys 0m2.032s
Notes: Well, it’s user+kernel cpu, for this class, because that’s what we can do something about.
But for the rest of the class, I’ll just say ET and you don’t have to think hard about what it means (ie, assume no other jobs, no stalls for disk, etc.)
Maybe: Note the ”time travel”. I.e. user > real in this example because of parallelism!
In case I forget: https://stackoverflow.com/questions/556405/what-do-real-user-and-sys-mean-in-the-output-of-time1
Real is wall clock time - time from start to finish of the call. This is all elapsed time including time slices used by other processes and time the process spends blocked (for example if it is waiting for I/O to complete).
User is the amount of CPU time spent in user-mode code (outside the kernel) within the process. This is only actual CPU time used in executing the process. Other processes and time the process spends blocked do not count towards this figure.
Sys is the amount of CPU time spent in the kernel within the process. This means executing CPU time spent in system calls within the kernel, as opposed to library code, which is still running in user-space. Like 'user', this is only CPU time used by the process. See below for a brief description of kernel mode (also known as 'supervisor' mode) and the system call mechanism.

## Slide 125: Execution Time
Processor A is faster than the processor B
Relative performance: Performance of A is n times greater than B

## Slide 126: How architects define Performance
Only has meaning in the context of a program or workload
Not very intuitive as an absolute measure, but most of the time we’re more interested in relative performance
PerformanceX =
1
Execution TimeX
, for program X

## Slide 127: Relative Performance
Can be confusing…
  A runs in 12 seconds
  B runs in 20 seconds
  A/B = .6 , so A is 40% faster, or 1.4X faster, or B is 40% slower
  B/A = 1.67, so A is 67% faster, or 1.67X faster, or B is 67% slower
Needs a precise definition
Notes: The a/b , b/a thing is just to make the point that the language can be confusing, and have seen lots of performance claims that use faulty terminology. So we need to all agree on how we are going to talk about relative performance.

## Slide 128: Relative Performance (Speedup), the Definition
PerformanceX
Execution TimeX
PerformanceY
Speedup
Execution TimeY
=
=
=
n
(X/Y)

## Slide 129: Example
Machine A runs program C in 9 seconds.
Machine B runs the same program in 6 seconds.
What is the speedup we see if we move to Machine B from Machine A?
Notes: I like to work problems in the class, with participation and help from the class. Now could also make this a “clicker question” or this quarter a “poll question”. But maybe better to do that on the second one after working the first.

## Slide 130: What is Time?
CPU Execution Time = CPU clock cycles * Clock cycle time
  Every conventional processor has a clock with an associated clock cycle time or clock rate
  Every program runs in an integral number (whole number) of clock cycles
Cycle Time
MHz = millions of cycles/second, GHz = billions of cycles/second
X MHz = 1000/X nanoseconds cycle time
Y GHz = 1/Y nanoseconds cycle time

## Slide 131: CPU time
CPU time is the time CPU is computing
  Not including followings
    Memory access time
    IO access time
CPU time = Clock cycles * Clock Period
Clock period = 1/Clock frequency
100 MHz of clock frequency = 10 ns of clock period
1GHz of clock frequency = 1 ns of clock period

## Slide 132: How many clock cycles?
Number of CPU clock cycles =
[Instruction count] * [Average Clock Cycles per Instruction (CPI)]
Exercise:
Computer A runs program C in 3.6 billion cycles.
Program C requires 2 billion dynamic instructions.
What is the CPI?
Notes: After example, ask why it is okay that CPI is not an integer? What does this imply about instructions in this machine?

## Slide 133: Clock Cycles Per Instruction (CPI)
CPI is the average number of clock cycles per instruction
  Throughput metric
  Component metric (not a measure of performance )
Different classes of instructions can have different CPIs
  CPI for floating point operations
  CPI for adders, branch instructions
CPU Clock Cycles = Number of Instructions (NI)* CPI
The CPI of ith class
The number of instructions of ith class

## Slide 134: Putting it all together
CPU Execution Time = [CPU clock cycles] * [Clock cycle time]
CPU clock cycles = [Instruction count] * [Average Clock Cycles per Instruction (CPI)]
CPU Execution Time
Instruction Count
CPI
Clock Cycle Time
=
X
X
instructions
cycles/instruction
seconds/cycle
seconds
Notes: Dimensional analysis

## Slide 135: CPU Execution Time
CPU Execution Time = CPU Clock Cycles * Clock Period
= NI*CPI*Clock Period
Execution time depends on
  Number of instructions : Determined by the ISA
    Programmable hardware counters can be used to find NI
    Profiling tools such as gprof, valgrind
  CPI: determined by the ISA & Compiler & Organization (Parallel execution)
    Can be determined in software using simulator
  Clock period: Determined by the process technology and implementation

## Slide 136: Cycle Time/Clock Rate is no longer fixed
Increasingly, modern processors can execute at multiple clock rates (cycle times).
Why?
However, the granularity at which we can change the cycle time tends to be fairly coarse, so all of these principles and formulas still apply.

## Slide 137: Who Affects Performance? How?
programmer
compiler
instruction-set architect
machine architect
hardware designer
materials scientist/physicist/silicon engineer
CPU Execution Time
Instruction Count
CPI
Clock Cycle Time
=
X
X
Notes: The perf slides and ET equation are key to the whole class.

## Slide 138: Which programs are best, are “most fair”, to run when measuring performance?
peak throughput measures (simple programs)?
synthetic benchmarks (whetstone, dhrystone,...)?
Real applications
SPEC (best of both worlds, but with problems of their own)
  System Performance Evaluation Cooperative
  Provides a common set of real applications
    Along with strict guidelines for how to run them
  Provides a relatively unbiased means to compare machines.

## Slide 139: Amdahl’s Law
The impact of a performance improvement is limited by the percent of execution time affected by the improvement
Make the common case fast!!
Execution time
after improvement
=
Execution Time Affected
Amount of Improvement
Execution Time Unaffected
+

## Slide 140: Amdahl’s Law and Massive Parallelism
.9
.1
Notes: I love this slide. If there is one other concept besides the ET equation I really want them to get, it is this. It explains why I spent most of my career using parallel hardware to make single thread performance fast.

## Slide 141: Amdahl’s Law and Massive Parallelism
.9
.1
.1
.45
Speedup
1.0
1/.55 = 1.82

## Slide 142: Amdahl’s Law and Massive Parallelism
.9
.1
.1
.1
.45
.225
Speedup
1.0
1/.55 = 1.82
1/.325 = 3.07

## Slide 143: Amdahl’s Law and Massive Parallelism
.9
.1
.1
.1
.1
.45
.225
Speedup
1.0
1/.55 = 1.82
1/.325 = 3.07
< 10
Notes: n.b. 1 / .19 = 5.26

## Slide 144: Key Points
Be careful how you specify performance
Execution time = instructions * CPI * cycle time
Use real applications
Use standards, if possible
Make the common case fast