## Slide 1: WES237B: Software for Embedded Systems
Pat Pannuto
Department of Computer Science and Engineering
University of California, San Diego
Summer Session 2022

## Slide 2: Today
Morning
  Performance & Optimization
  Optimization in different levels (in the context of a single core)
    Algorithmic (Cache Optimization), Compiler and Hardware
    Memory Hierarchy
Afternoon
  Lab session

## Slide 3: Logistics
Assignment 1 due tomorrow
Assignment 2 released
  Generally: First bit of assignment is lab portion, the rest is take-home
  Finish the lab first if needed
Late policy?
  1 week: 10% off
  2 weeks: Last chance, 30% off
  Email with any exceptional circumstances, we’ll work it out
Sign up for presentation slots!

## Slide 4: Recap
Embedded Systems (SoC) Design
ARM processor technology
  ISA: ARMv4, ARMv5, ARMv6, ARMv7, ARMv8
  Cortex-A5,6,7,…15
Processor Types
  Microcontrollers, DSP, FPGA, GPU,…
Huffman Encoding

## Slide 5: The guts of most interesting stuff is often ~this
void Foo(float* const A, float* const B, float* const C, const int M, const int N, const int K)
{
  for (int m = 0; m < M; m++) {
    for (int n = 0; n < N; n++) {
      for (int k = 0; k < K; k++) {
        C[m * M + n] += A[m * M + k] * B[k * K + n];
      }
    }
  }
}
Notes: Not literally these loops, but multi-dimensional math, which boils down to loops of basic op’s marching through arrays

## Slide 6: Measuring Performance
Notes: What are the goals of Software Optimization ?

## Slide 7: The bottom line: Performance
Time to do the task
  execution time, response time, latency
Tasks per day, hour, week, sec, ns. ..
  throughput, bandwidth
Ferrari
Bus
Speed
160 mph
65 mph
Time to Bay Area
3.1 hours
7.7 hours
Passengers
2
60
Throughput (pmph)
320
3900

## Slide 8: Measures of “Performance”
Execution Time
Throughput (operations/time)
  Transactions/sec, queries/day, etc.
Frame Rate
Responsiveness
Performance / Cost
Performance / Power
Performance / Energy
Different Metrics for different folks
ET is standard responsiveness
Frame Rate – FPS/Media App
Throughput (Servers)
Responsiveness – similar to ET but can vary, think ipod/smartphone
Perf/Cost – Server farm / everyone
Perf/Power – power is expensive and causes thermal issues(cooling)
Perf/Energy – battery-based designs

## Slide 9: Why Study Computer Performance?
In order to say X is n times faster than Y
Identify the benefits of running a program on a computer X, or bottlenecks of a program on a computer X
Embedded systems are too complex (CPU + FPGA + GPU)  How to measure performance of system consisting of sequential and parallel parts ?
To understand common techniques to measure performance
To know what to measure & how to measure

## Slide 10: Performance is Affected by,…

## Slide 11: Performance is Affected by,…
Technology
  Clock speed
  Processor technology

## Slide 12: Performance is Affected by,…
Technology
  Clock speed
  Processor technology
Organization
  Single core. vs. multi core
  Types of processors implementation (SIMD, out of order,..)
  Heterogeneous (SoC)
  Memory hierarchy & memory type
  Type of I/O devices
  ,…

## Slide 13: Performance is Affected by,…
Technology
  Clock speed
  Processor technology
Organization
  Single core. Vs. multi core
  Heterogeneous (SoC)
  Types of processors (SIMD, out of order,..)
  Memory hierarchy & memory type
  Type of I/O devices
  ,…
Software
  Quality of compilers & libraries & parallel processing frameworks
  Operating system

## Slide 14: Principles of Measuring Performance
Well defined metrics
  Execution time = Time spent running a program on X computer
Reproducibility
  Should get the same result when you are using the same program on same machine under same conditions (OS, compiler levels,…)
Standard Benchmarks
  SPEC (https://www.spec.org/benchmarks.html)

## Slide 15: Performance Metrics
Raw speed = peak performance
  In practice, never attainable
  Clock rate * #of floating point operations/cycle (E.g., 10 Gflops)
Execution time = time to execute a program from beginning to end
  The sooner the better
  Wall clock time/elapsed time: Time to complete task as seen by the user. Might include operating system overhead or interference with other applications
  CPU Time: does not include time spent for IO, external sources
    User CPU time: CPU time spent in the program
    System CPU time: CPU time spent in the OS performing taks requested by program
Throughput = total amount of work completed in a given time
  Frames per second (fps)., 30 fps
  Transactions or packets per second
  Indication of how well hardware resources are being used
Memory: Bandwidth & Latency

## Slide 16: There are many ways to measure program execution time
Program-reported time?
Wall-clock time?
user CPU time?
user + kernel CPU time?
$ time make # cargo build
Compiling hail v0.1.0 (/tock/boards/hail)
Finished release [optimized + debuginfo] target(s) in 19.96s
real 0m21.146s
user 0m30.388s
sys 0m2.032s
Notes: Well, it’s user+kernel cpu, for this class, because that’s what we can do something about.
But for the rest of the class, I’ll just say ET and you don’t have to think hard about what it means (ie, assume no other jobs, no stalls for disk, etc.)
Maybe: Note the ”time travel”. I.e. user > real in this example because of parallelism!
In case I forget: https://stackoverflow.com/questions/556405/what-do-real-user-and-sys-mean-in-the-output-of-time1
Real is wall clock time - time from start to finish of the call. This is all elapsed time including time slices used by other processes and time the process spends blocked (for example if it is waiting for I/O to complete).
User is the amount of CPU time spent in user-mode code (outside the kernel) within the process. This is only actual CPU time used in executing the process. Other processes and time the process spends blocked do not count towards this figure.
Sys is the amount of CPU time spent in the kernel within the process. This means executing CPU time spent in system calls within the kernel, as opposed to library code, which is still running in user-space. Like 'user', this is only CPU time used by the process. See below for a brief description of kernel mode (also known as 'supervisor' mode) and the system call mechanism.

## Slide 17: Execution Time
Processor A is faster than the processor B
Relative performance: Performance of A is n times greater than B

## Slide 18: How architects define Performance
Only has meaning in the context of a program or workload
Not very intuitive as an absolute measure, but most of the time we’re more interested in relative performance
PerformanceX =
1
Execution TimeX
, for program X

## Slide 19: Relative Performance
Can be confusing…
  A runs in 12 seconds
  B runs in 20 seconds
  A/B = .6 , so A is 40% faster, or 1.4X faster, or B is 40% slower
  B/A = 1.67, so A is 67% faster, or 1.67X faster, or B is 67% slower
Needs a precise definition
Notes: The a/b , b/a thing is just to make the point that the language can be confusing, and have seen lots of performance claims that use faulty terminology. So we need to all agree on how we are going to talk about relative performance.

## Slide 20: Relative Performance (Speedup), the Definition
PerformanceX
Execution TimeX
PerformanceY
Speedup
Execution TimeY
=
=
=
n
(X/Y)

## Slide 21: Example
Machine A runs program C in 9 seconds.
Machine B runs the same program in 6 seconds.
What is the speedup we see if we move to Machine B from Machine A?
Notes: I like to work problems in the class, with participation and help from the class. Now could also make this a “clicker question” or this quarter a “poll question”. But maybe better to do that on the second one after working the first.

## Slide 22: What is Time?
CPU Execution Time = CPU clock cycles * Clock cycle time
  Every conventional processor has a clock with an associated clock cycle time or clock rate
  Every program runs in an integral number (whole number) of clock cycles
Cycle Time
MHz = millions of cycles/second, GHz = billions of cycles/second
X MHz = 1000/X nanoseconds cycle time
Y GHz = 1/Y nanoseconds cycle time

## Slide 23: CPU time
CPU time is the time CPU is computing
  Not including followings
    Memory access time
    IO access time
CPU time = Clock cycles * Clock Period
Clock period = 1/Clock frequency
100 MHz of clock frequency = 10 ns of clock period
1GHz of clock frequency = 1 ns of clock period

## Slide 24: How many clock cycles?
Number of CPU clock cycles =
[Instruction count] * [Average Clock Cycles per Instruction (CPI)]
Exercise:
Computer A runs program C in 3.6 billion cycles.
Program C requires 2 billion dynamic instructions.
What is the CPI?
Notes: After example, ask why it is okay that CPI is not an integer? What does this imply about instructions in this machine?

## Slide 25: Clock Cycles Per Instruction (CPI)
CPI is the average number of clock cycles per instruction
  Throughput metric
  Component metric (not a measure of performance )
Different classes of instructions can have different CPIs
  CPI for floating point operations
  CPI for adders, branch instructions
CPU Clock Cycles = Number of Instructions (NI)* CPI
The CPI of ith class
The number of instructions of ith class

## Slide 26: Putting it all together
CPU Execution Time = [CPU clock cycles] * [Clock cycle time]
CPU clock cycles = [Instruction count] * [Average Clock Cycles per Instruction (CPI)]
CPU Execution Time
Instruction Count
CPI
Clock Cycle Time
=
X
X
instructions
cycles/instruction
seconds/cycle
seconds
Notes: Dimensional analysis

## Slide 27: CPU Execution Time
CPU Execution Time = CPU Clock Cycles * Clock Period
= NI*CPI*Clock Period
Execution time depends on
  Number of instructions : Determined by the ISA
    Programmable hardware counters can be used to find NI
    Profiling tools such as gprof, valgrind
  CPI: determined by the ISA & Compiler & Organization (Parallel execution)
    Can be determined in software using simulator
  Clock period: Determined by the process technology and implementation

## Slide 28: Cycle Time/Clock Rate is no longer fixed
Increasingly, modern processors can execute at multiple clock rates (cycle times).
Why?
However, the granularity at which we can change the cycle time tends to be fairly coarse, so all of these principles and formulas still apply.

## Slide 29: Who Affects Performance? How?
programmer
compiler
instruction-set architect
machine architect
hardware designer
materials scientist/physicist/silicon engineer
CPU Execution Time
Instruction Count
CPI
Clock Cycle Time
=
X
X
Notes: The perf slides and ET equation are key to the whole class.

## Slide 30: Which programs are best, are “most fair”, to run when measuring performance?
peak throughput measures (simple programs)?
synthetic benchmarks (whetstone, dhrystone,...)?
Real applications
SPEC (best of both worlds, but with problems of their own)
  System Performance Evaluation Cooperative
  Provides a common set of real applications
    Along with strict guidelines for how to run them
  Provides a relatively unbiased means to compare machines.

## Slide 31: Amdahl’s Law
The impact of a performance improvement is limited by the percent of execution time affected by the improvement
Make the common case fast!!
Execution time
after improvement
=
Execution Time Affected
Amount of Improvement
Execution Time Unaffected
+

## Slide 32: Amdahl’s Law and Massive Parallelism
.9
.1
Notes: I love this slide. If there is one other concept besides the ET equation I really want them to get, it is this. It explains why I spent most of my career using parallel hardware to make single thread performance fast.

## Slide 33: Amdahl’s Law and Massive Parallelism
.9
.1
.1
.45
Speedup
1.0
1/.55 = 1.82

## Slide 34: Amdahl’s Law and Massive Parallelism
.9
.1
.1
.1
.45
.225
Speedup
1.0
1/.55 = 1.82
1/.325 = 3.07

## Slide 35: Amdahl’s Law and Massive Parallelism
.9
.1
.1
.1
.1
.45
.225
Speedup
1.0
1/.55 = 1.82
1/.325 = 3.07
< 10
Notes: n.b. 1 / .19 = 5.26

## Slide 36: Optimizations
Notes: 2021: 10:05 am

## Slide 37: What to optimize on a CPU?
Program type
  Compute-bound
  I/O bound
 | Number of Instructions (NI) | CPI | Clock Frequency
Program |  |  | 
Compiler |  |  | 
ISA |  |  | 
Organization |  |  | 
Technology |  |  | 
CPU Execution Time = CPU Clock Cycles * Clock Period
= NI*CPI*Clock Period
Reduce Clock Period  Increase clock frequency
Decrease NI
Decrease CPI

## Slide 38: Optimization is
An application X  optimize it on Y?
  Where should I start?
  When I know if I hit the target performance (or do I have a target performance)?
hard
Both system level and low-level knowledge/experience is needed
system level  Algorithmic, Compiler, Multi-core,…
Low-level Cache organization, compiler optimization,…

## Slide 39: Optimization is hard (and getting harder…)
Must understand system as a whole to optimize
Software Application
Compiler
Hardware (A GPU)
Algorithmic Optimization
Big O(n2)  Big O(nlogn)
Arithmetic optimizations
Algorithmic changes that uses HW efficiently
..
Loop vectorization
Constant subexpression elimination
,…
Micro architectural design
Frequency/Clock cycles
Instruction level parallelism…
Cache optimization..
Possible #of total optimization space = #algorithms * compiler optimization* # hardware optimizations  Optimization search space

## Slide 41: Optimization is hard (and getting harder…)
Must understand system as a whole to optimize
Software Application
Compiler
Algorithmic Optimization
Big O(n2)  Big O(nlogn)
Arithmetic optimizations
Algorithmic changes that uses HW efficiently
..
Loop vectorization
Constant subexpression elimination
,…
Micro architectural design,
Frequency/Clock cycles
Instruction level parallelism…
Cache optimization..
Hardware (A GPU)
Hardware (A GPU)
Hardware (A GPU)
[ or TPU or …]
Heterogenous (or system with multiple hardware units)  optimization parameter search space is large

## Slide 42: Optimizations in Different Levels
Software
Hardware
ISA
Pipelining, out-of-order execution,
Branch prediction, superscalar,
Cache organization, multi-core,…
Multithreading, Inline Assembly,
Blocking, Loop interchange,..etc.
Compiler level optimizations such
as dead code elimination, ..
Optimization: Must optimize at multiple levels:
Algorithm level, data representations, procedures, compiler, and hardware,...

## Slide 43: Optimizations
Must understand system as a whole to optimize for performance
How programs are compiled and executed
How modern processors + memory systems operate
How to measure program performance and identify bottlenecks
How to improve performance without destroying code modularity and generality

## Slide 44: Micro Architecture
Notes: 2021: 11:13 am

## Slide 45: Instruction Level Parallelism
Need general understanding of modern processor design
Hardware can execute multiple instructions in parallel
Performance limited by data dependencies
Simple transformations can yield dramatic performance improvement
Compilers often (sometimes) cannot make these transformations
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 46: Superscalar processor
A superscalar processor can issue and execute multiple instructions in one cycle. The instructions are retrieved from a sequential instruction stream and are usually scheduled dynamically.
Benefit: without programming effort, superscalar processor can take advantage of the instruction level parallelism that most programs have
Most modern CPUs are superscalar
Intel: since Pentium (1993)
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 47: Pipelined Functional Units
Stage 1
Stage 2
Stage 3
long mult_eg(long a, long b, long c) {
long p1 = a*b; long p2 = a*c; long p3 = p1 * p2;
return p3; }
  Divide computation into stages
  Pass partial computations from stage to stage
  Stage i can start on new computation once values passed to i+1
  E.g., complete 3 multiplications in 7 cycles, even though each requires 3 cycles
​ | Time​ |  |  |  |  |  | 
​ | 1​ | 2​ | 3​ | 4​ | 5​ | 6​ | 7​
Stage 1​ | a*b​ | a*c​ | ​ | ​ | p1*p2​ | ​ | ​
Stage 2​ | ​ | a*b​ | a*c​ | ​ | ​ | p1*p2​ | ​
Stage 3​ | ​ | ​ | a*b​ | a*c​ | ​ | ​ | p1*p2​
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 48: Haswell CPU
Multiple instructions can execute in parallel
  2 load, with address computation
  1 store, with address computation
  4 integer
  2 FP multiply
  1 FP add
  1 FP divide
Some instructions take > 1 cycle, but can be pipelined
  Instruction Latency Cycles/Issue
  Load / Store 4 1
  Integer Multiply 3 1
  Integer/Long Divide 3-30 3-30
  Single/Double FP Multiply 5 1
  Single/Double FP Add 3 1
  Single/Double FP Divide 3-15 3-15
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 49: SIMD (Single Instruction Multiple Data)
SIMD Operations: Single Precision
%zmm0
%zmm1
vaddsd %zmm0, %zmm1, %zmm1
+
+
+
+
+
+
+
+
+
+
+
+
%zmm0
%zmm1
vaddds %zmm0, %zmm1, %zmm1
SIMD Operations: Double Precision
Example AVX-512F (a subset of AVX-512) instructions (ARM case Neon)
zmm0 ...zmm31 are 512 bit registers; each can hold
  16 single-precision (float of C; 32 bits) or
  8 double-precision (double of C; 64 bits) ﬂoating point numbers
Operation | Syntax
* | vmulps %zmm0,%zmm1,%zmm2
+ | vaddps %zmm0,%zmm1,%zmm2
 | ….
Float + | vfmadd132ps %zmm0,%zmm1,%zmm2
load | vmovups 256(%rax),%zmm0
Store | vmovups %zmm0,256(%rax)

## Slide 50: ARM Matrix Multiplication with SIMD
https://developer.arm.com/documentation/102467/0100/Matrix-multiplication-example

## Slide 51: The Memory Hierarchy

## Slide 52: Random-Access Memory (RAM)
RAM is traditionally packaged as a chip
Basic storage unit is a cell(one bit)
Multiple RAM chips form a memory
Types: Static RAM, Dynamic RAM
DRAM/SRAM are volatile memories
 | Trans per bit | Access Time | Needs Refresh | Cost | Application
SRAM | 4/6 | 1X | No | 100X | Cache memories/Scratch pad
DRAM | 1 | 10X | Yes | 1X | Main memories, frame buffers
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 53: Processor and Memory Gap
HP, Computer Architecture A Quantitate Approach, 2011

## Slide 54: Processor and Memory Gap
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 55: Processor and Memory Power Consumption
The energy consumption for various arithmetic operations and memory accesses in a 45 nm
process.
Sze, Vivienne, et al. "Efficient Processing of Deep Neural Networks." Synthesis Lectures on Computer Architecture 15.2 (2020): 1-341.

## Slide 56: Slow memory, faster processor: What can we do?

## Slide 57: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 58: Locality Example
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;

## Slide 59: C Memory
C is row major order ==> Meaning that if you have 2D array ==> Row 0, Row 1, Row 2,…. Row N.

## Slide 60: Locality Example
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Does these functions have good locality with respect to array a[]?

## Slide 61: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
They suggest an approach (trade-off) for organizing memory and storage systems known as a memory hierarchy.
Trade-off

## Slide 62: Memory Hierarchies
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 63: A Modern Memory Hierarchy
Register File, 32 words, sub-nsec
L1 Cache, ~32 KB, ~nsecs
L2 cache, 512KB – 1 MB, ~nsecs
L3 Cache, ~ 10 nsecs
Main memory (DRAM), GB, ~100 ns
Disk, 100 GB, ~10 msec

## Slide 64: Cache
(next time)