## Slide 1: WES237B: Software for Embedded Systems
Pat Pannuto
Department of Computer Science and Engineering
University of California, San Diego
Summer Session 2022

## Slide 2: Today
Morning
  Parallel Programming Patterns
  Streaming Programming Patterns
  Deep Learning (Lite)
Afternoon+
  Lab session
    Applied Deep Learning
  Assignment
    Ain’t that a question

## Slide 3: Logistics
Assignment 4 due tomorrow
Assignment 5 released
  Generally: First bit of assignment is lab portion, the rest is take-home
  Finish the lab first if needed
Late policy?
  1 week: 10% off
  2 weeks: Last chance, 30% off
  Email with any exceptional circumstances, we’ll work it out

## Slide 4: Recap
SIMD, SPMD, MIMD & Flynn’s Taxonomy
  Ways to describe ‘how parallel’ execution is
  Expresses hardware capability, software engineer has to figure how to use it well
CUDA
  Varying units of parallelism and flexibility
  Threads, warps, blocks, grids
CUDA Memory
  Performance highly dependent on memory management
  Still heavily manual process :/

## Slide 5: Limitations of Optimizing Compilers
Operate under fundamental constraint
Must not cause any change in program behavior
Except, possibly when program making use of nonstandard language features
Behavior that may be obvious to the programmer can be obfuscated by languages and coding styles
e.g., Data ranges may be more limited than variable types suggest
Most analysis is performed only within procedures
Whole-program analysis is too expensive in most cases
Newer versions of GCC do interprocedural analysis within individual files
But, not between code in different files
Most analysis is based only on static information
Compiler has difficulty anticipating run-time inputs
When in doubt, the compiler must be conservative​
Bryant and O'Hallaron, Computer Systems: A programmer's Perspective

## Slide 6: The guts of most interesting stuff is often ~this
void Foo(float* const A, float* const B, float* const C, const int M, const int N, const int K)
{
  for (int m = 0; m < M; m++) {
    for (int n = 0; n < N; n++) {
      for (int k = 0; k < K; k++) {
        C[m * M + n] += A[m * M + k] * B[k * K + n];
      }
    }
  }
}
And these are huge
Lab2: image.tif
480x640 pixels * 4 bytes/float ~= 1.3 MB (greyscale!)
Notes: Not literally these loops, but multi-dimensional math, which boils down to loops of basic op’s marching through arrays

## Slide 7: Parallel Programming Patterns
… could we not deal with all this HW knowledge, please?

## Slide 8: Frequency Scaling

## Slide 9: Floating-Point Operations/Second

## Slide 10: Frequency vs. Parallelism
Single CPU performance
  Doubled every 2 years for 30 years; stopped around 2006
  Marginal improvement since around 2006
Solution  Parallelism (Heterogeneous Parallel Programming)
ARM +FPGA
ARM +GPU
ARM +Graphics Processor + FPGA
Does (Heterogeneous) Parallel Programming Matter for Embedded Systems ?

## Slide 11: Parallelism ?
Parallelism is achieved by partitioning or decomposing an application into serial & parallel parts
How to know where the parallelism is?
How to write parallel programs?

## Slide 12: Parallelism  Decomposition
Defining Requirements
Defining Specification
Partition
Sequential
Parallel
System Integration & Testing
Application

## Slide 13: Parallel Programming is

## Slide 14: Parallel Programming is Difficult!

## Slide 15: Some are harder than others,..
void vecvecmul(int N,int *a, int *b, int *c){
int b=0,a=0;
int sum=0;
for(int i=0;i<N;i++){
c[i]=a[i]*b[i];
}

## Slide 16: Some are harder than others,..
void vecvecmul(int N,int *a, int *b, int *c){
int b=0,a=0;
int sum=0;
for(int i=0;i<N;i++){
c[i]=a[i]*b[i];
}
void prefixsum(int in[SIZE], int out[SIZE]){
out[0] = in[0];
for(int i = 1; i < SIZE; ++i)
{
out[i] = out[i-1] + in[i];
}
}

## Slide 17: Some are harder than others,..
void vecvecmul(int N,int *a, int *b, int *c){
int b=0,a=0;
int sum=0;
for(int i=0;i<N;i++){
c[i]=a[i]*b[i];
}
void Foo(DTYPE numbers[n])
{
int i, j, index;
for (i=1; i < n; i++)
{
index = numbers[i];
j = i;
while ((j > 0)&& (numbers[j-1] > index) )
{
numbers[j] = numbers[j-1];
j = j - 1;
}
numbers[j] = index;
}
}
void prefixsum(int in[SIZE], int out[SIZE]){
out[0] = in[0];
for(int i = 1; i < SIZE; ++i)
{
out[i] = out[i-1] + in[i];
}
}

## Slide 18: A Number of Platforms and Programming Models
Platforms
  Multicores
  GPUs
  FPGAs
  …
Programming models, libraries & languages
  CPU
    Pthreads
    OpenMP
  GPU
    CUDA
    OpenCL
  FPGA
    Models: streaming, pipeline, dataflow pipeline,…
    Languages: Verilog, VHDL, HLS, OpenCL, Chisel, FCUDA

## Slide 19: Mapping serial application to parallel platform
Automatic to some degree
Parallel Programming Environment Another Parallel Programming environment
Manually decomposing parallelism & Mapping it into a parallel platform
Application
Parallel Platform
(GPU or FPGA or,..CPU)

## Slide 20: Mapping serial application to parallel platform
Application
Parallel Platform
(GPU or FPGA or,..CPU)
Automatic to some degree (usually using pragmas)
E.g., OpenMP or HLS

## Slide 21: Mapping serial application to parallel platform
Application
Parallel Platform
(GPU or FPGA or,..CPU)
Automatic to some degree (usually using pragmas)
E.g., OpenMP or HLS
void vecvecmul(int N,int *a, int *b, int *c){
int b=0,a=0;
int sum=0;
for(int i=0;i<N;i++){
c[i]=a[i]*b[i];
}

## Slide 22: Mapping serial application to parallel platform
__global__ void saxpy(int n, float a, float *x, float *y)
{
int i = blockIdx.x*blockDim.x + threadIdx.x;
if (i < n) y[i] = a*x[i] + y[i];
}
OpenMPCUDA
CPU Code
CUDA Code

## Slide 23: Mapping serial application to parallel platform
void Foo(DTYPE numbers[n])
{
int i, j, index;
for (i=1; i < n; i++)
{
index = numbers[i];
j = i;
while ((j > 0)&& (numbers[j-1] > index) )
{
numbers[j] = numbers[j-1];
j = j - 1;
}
numbers[j] = index;
}
}
Parallel Platform
(GPU or FPGA or,..CPU)
Most of the time programmer must modify the code so that it maps well to target platform  Difficult, time consuming
There are some best practices & and parallel programming models

## Slide 24: Structured Parallel Patterns
The following additional parallel patterns can be used for “structured parallel programming”:
  Superscalar sequence
  Speculative selection
  Map
  Recurrence
  Scan
  Reduce
  Pack/expand
  Fork/join
  Pipeline
  Partition
  Segmentation
  Stencil
  Search/match
  Gather
  Merge scatter
  Priority scatter
  *Permutation scatter
  !Atomic scatter
Using these patterns, threads and vector intrinsics can (mostly) be eliminated and the maintainability of software improved.
24
This slide is from :McCool et al, “Structured Parallel Programming: Patterns for Efficient Computation” – Full Presentation
Notes: Most mutexes and semaphores can be eliminated too. Semaphores are truly the “goto” of parallel programming, since a “signal” operation causes a “wait” operation somewhere else to return.

## Slide 25: Parallel Patterns
Parallel Pattern for Convolution
Parallel Pattern for Prefix sum
Parallel Pattern for Histogram Computation
Parallel Pattern for Sparse Matrix Computation
Parallel Pattern for Merge/Quick Sort

## Slide 26: Parallel Programming Patterns
f
Fork/Join
Bulk Synchronous
MapReduce
Sliding Window
Reduction
Blocking

## Slide 27: Blocking: Matrix*Matrix operations
a12
a11
a14
a13
a22
a21
a24
a23
b12
b11
b22
b21
b32
b31
b42
b41
stream 1
stream 2
a11*b11
a12*b21
a13*b31
a14*b41
+
+
+
=
a11*b12
a12*b22
a13*b32
a14*b42
+
+
+
=
c12
c11
a21*b11
a22*b21
a23*b31
a24*b41
+
+
+
=
a21*b12
a22*b22
a23*b32
a24*b42
+
+
+
=
c22
c21
a12
a11
a14
a13
a22
a21
a24
a23
a32
a31
a34
a33
a42
a41
a44
a43
b12
b11
b14
b13
b22
b21
b24
b23
b32
b31
b34
b33
b42
b41
b44
b43
c12
c11
c14
c13
c22
c21
c24
c23
c32
c31
c34
c33
c42
c41
c44
c43
x

## Slide 28: Prefix sum Serial Code
void prefixsum(I_TYPE in[SIZE], I_TYPE out[SIZE]){
for(int i = 1; i < SIZE; ++i){
out[i] = out[i-1] + in[i];
}
}
0
2
1
6
3
1
2
5
0
2
3
9
12
13
15
20
Input:
Output:

## Slide 29: Parallel Pattern for Prefix Sum
0
2
1
6
3
1
2
5
0
2
3
7
9
4
3
7
0
2
3
9
12
11
12
11
0
2
3
9
12
13
15
20
temp1
temp2
temp3
Stage 1
Stage 2
Stage 3

## Slide 30: Mapping to BulkSynchronous Pattern
1 | 2 | 3
0 | 0 | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1
1 | 2 | 3
 |  | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1
1 | 1 | 1
0 | 0 | 2
1 | 2 | 3
9 | 9 | 9
6 | 0 | 9
6 | 0 | 9
0 | 0 | 2
1 | 1 | 1
1 | 2 | 3
9 | 9 | 9
0 | 0 | 2
1 | 1 | 1
1 | 2 | 3
6 | 0 | 9
9 | 9 | 9

## Slide 31: Mapping to BulkSynchronous Pattern
1. Counting sort
2. Counting sort
3. Counting sort
4. Counting sort
(b) Radix sort
Mem(n)
Mem(n)
Mem(n)
1 | 2 | 3
0 | 0 | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1
1 | 2 | 3
 |  | 2
9 | 9 | 9
6 | 0 | 9
1 | 1 | 1
1 | 1 | 1
0 | 0 | 2
1 | 2 | 3
9 | 9 | 9
6 | 0 | 9
6 | 0 | 9
0 | 0 | 2
1 | 1 | 1
1 | 2 | 3
9 | 9 | 9
0 | 0 | 2
1 | 1 | 1
1 | 2 | 3
6 | 0 | 9
9 | 9 | 9

## Slide 32: Mapping serial application to parallel platform
void InsertionSort(DTYPE numbers[n])
{
int i, j, index;
for (i=1; i < n; i++)
{
index = numbers[i];
j = i;
while ((j > 0)&& (numbers[j-1] > index) )
{
numbers[j] = numbers[j-1];
j = j - 1;
}
numbers[j] = index;
}
}
Parallel Platform
(GPU or FPGA or,..CPU)
Serial Code  Streaming Models

## Slide 33: Streaming Programming ?

## Slide 34: Insertion Sort
2
5
1
3

## Slide 35: Insertion Sort
2
5
1
3

## Slide 36: Insertion Sort
3
2
5
1
2
5
1
3

## Slide 37: Insertion Sort
3
2
5
1
2
5
1
3

## Slide 38: Insertion Sort
3
2
5
1
2
5
1
3
2
3
5
1

## Slide 39: Insertion Sort
3
2
5
1
2
5
1
3
2
3
5
1

## Slide 40: Insertion Sort
3
2
5
1
2
5
1
3
2
3
5
1
2
3
5
1

## Slide 41: Insertion Sort
3
2
5
1
2
5
1
3
2
3
5
1
2
3
5
1

## Slide 42: Insertion Sort
3
2
5
1
2
5
1
3
2
3
5
1
2
3
5
1
1
2
3
5
void InsertionSort(DTYPE numbers[n])
{
int i, j, index;
for (i=1; i < n; i++)
{
index = numbers[i];
j = i;
while ((j > 0)&& (numbers[j-1] > index) )
{
numbers[j] = numbers[j-1];
j = j - 1;
}
numbers[j] = index;
}
}

## Slide 43: Insertion Sort: Streaming

## Slide 44: Insertion Sort: Streaming
2
5
1
3
2
5
1
3

## Slide 45: Insertion Sort: Streaming
2
5
1
3

## Slide 46: Insertion Sort: Streaming
5
1
3
2

## Slide 47: Insertion Sort: Streaming
5
1
3
2

## Slide 48: Insertion Sort: Streaming
5
1
3
2

## Slide 49: Insertion Sort: Streaming
1
2
5
3

## Slide 50: Insertion Sort: Streaming
2
5
1
3
2
5
1
3
Streaming Core
There is a plethora of work on parallel soring algorithms (computational patterns are very different from what we learned from
Our algorithms class)
Bitonic sort, parallel merge (quick) sort,…

## Slide 51: Sliding Window: Convolution
Magnification
-1 | 0 | +1
-2 | 0 | +2
-1 | 0 | +1
+1 | +2 | +1
0 | 0 | 0
-1 | -2 | -1
G_X = 1*(-1) + 2*0 + 3*1 +…+ = 8
G_Y = 1*(-1) + 2*2 +3*1 + … + = -32
for(int i = 0; i < rows; i++){
for(int j=0; j < cols; j++){
Gx = 0;
Gy = 0;
for(int rowOffset = -1; rowOffset <= 1; rowOffset++){
for(int colOffset = -1; colOffset <=1; colOffset++){
Gx = Gx + …;
Gy = Gy + …;
G = …;
}
}
}
}
G=sqrt(G_X2 + G_Y2)

## Slide 52: Sliding Window: Convolution
Based on Xilinx tutorial: “Zynq all programmable soc sobel filter implementation using the vivado hls tool.”
for(int i = 0; i < rows; i++){
for(int j=0; j < cols; j++){
Gx = 0;
Gy = 0;
for(rowOffset = -1; rowOffset <= 1; rowOffset++){
for(colOffset = -1; colOffset <=1; colOffset++){
Gx = Gx + …;
Gy = Gy + …;
G = …;
}
}
}
}

## Slide 53: Sliding Window: Convolution
Input Image
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Line Buffer
Window Buffer
Kernel
Computation
New data
1
2
3
5
6
7
9
10
11
Window Buffer 1

## Slide 54: Sliding Window: Convolution
Line Buffer
Window Buffer
Kernel
Computation
New data
Input Image
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
2
3
6
7
10
11
Window Buffer 2
4
8
12
1
2
3
5
6
7
9
10
11
Window Buffer 1

## Slide 55: Sliding Window: Convolution
Line Buffer
Window Buffer
Kernel
Computation
New data
Input Image
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
2
3
6
7
10
11
Window Buffer 2
4
8
12
1
2
3
5
6
7
9
10
11
Window Buffer 1
1
2
3
4
5
6
7
8
9
10
11
12
Line Buffer at time t
Line 1
Line 2
Line 3

## Slide 56: Sliding Window: Convolution
Line Buffer
Window Buffer
Kernel
Computation
New data
Input Image
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
2
3
6
7
10
11
Window Buffer 2
4
8
12
1
2
3
5
6
7
9
10
11
Window Buffer 1
1
2
3
4
5
6
7
8
9
10
11
12
Line Buffer at time t
Line 1
Line 2
Line 3

## Slide 57: Sliding Window: Convolution
Line Buffer
Window Buffer
Kernel
Computation
New data
Input Image
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
2
3
6
7
10
11
Window Buffer 2
4
8
12
1
2
3
5
6
7
9
10
11
Window Buffer 1
1
2
3
4
5
6
7
8
9
10
11
12
Line Buffer at time t
Line Buffer at time 0
Line 1
Line 2
Line 3

## Slide 58: Sliding Window: Convolution
Line Buffer
Window Buffer
Kernel
Computation
New data
2
3
6
7
10
11
Window Buffer 2
4
8
12
1
2
3
5
6
7
9
10
11
Window Buffer 1
1
2
3
4
5
6
7
8
9
10
11
12
Line Buffer at time t
Input Image
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Line Buffer at time 0
Line 1
Line 2
Line 3
1

## Slide 59: Sliding Window: Convolution
Line Buffer
Window Buffer
Kernel
Computation
New data
2
3
6
7
10
11
Window Buffer 2
4
8
12
1
2
3
5
6
7
9
10
11
Window Buffer 1
1
2
3
4
5
6
7
8
9
10
11
12
Line Buffer at time t
Input Image
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Line Buffer at time 0
Line 1
Line 2
Line 3
1
2
In GPU, Convolution is usually done using matrix multiplication

## Slide 60: Scalability & Portability
Scalability
  The same application runs efficiently on new generations of cores
  The same application runs efficiently on more of the same cores
  The same application runs on hardware with different number of resources
Portability
  The same application runs efficiently on hardware with different number of resources

## Slide 61: Deep Learning in half a morning 

## Slide 62: Deep Learning
Output layer
Hidden layers
Input layer
Deep Learning
“Seven”

## Slide 63: Deep Learning
Output layer
Hidden layers
Input layer
Deep Learning
“Seven”

## Slide 64: Deep Learning
Output layer
Hidden layers
Input layer
“Seven”
Neural Networks

## Slide 65: Deep Learning
Jth
Output layer
Hidden layers
Input layer
“Seven”
Neural Networks

## Slide 66: The Neuron Model
x1
x2
xn
w1j
w2j
wnj
yj

## Slide 67: Deep Learning
Output layer
Hidden layers
Input layer
“Seven”
Learning  Adjusting Weights!
W1
W2
W3

## Slide 68: Learning: Neural Network
Learning  Adjusting Weights!
x1 | x2 | s | y=f(s) | Output
0 | 0 |  |  | 0
0 | 1 |  |  | 0
1 | 0 |  |  | 0
1 | 1 |  |  | 1
AND
x2
x1
+1
w01
w11
w12
s=1*w01+x1*w11+x2*w12
f(s) =
f(-4.6) ~ 0 & f(4.6) ~ 1
y=f(s)

## Slide 69: Learning: Neural Network
Learning  Adjusting Weights!
x1 | x2 | s | y=f(s) | Output
0 | 0 |  |  | 0
0 | 1 |  |  | 0
1 | 0 |  |  | 0
1 | 1 |  |  | 1
AND
x2
x1
+1
w01=10
w11=10
w12=10
s=1*10+x1*10+x2*10
f(s) =
f(-4.6) ~ 0 & f(4.6) ~ 1
y=f(s)

## Slide 70: Learning: Neural Network
Learning  Adjusting Weights!
x1 | x2 | s | y=f(s) | Output
0 | 0 | 10 |  | 0
0 | 1 | 20 |  | 0
1 | 0 | 20 |  | 0
1 | 1 | 30 |  | 1
AND
x2
x1
+1
w01=10
w11=10
w12=10
s=1*10+x1*10+x2*10
f(s) =
f(-4.6) ~ 0 & f(4.6) ~ 1
y=f(s)

## Slide 71: Learning: Neural Network
Learning  Adjusting Weights!
x1 | x2 | s | y=f(s) | Output
0 | 0 | 10 | 1 | 0
0 | 1 | 20 | 1 | 0
1 | 0 | 20 | 1 | 0
1 | 1 | 30 | 1 | 1
AND
x2
x1
+1
w01=10
w11=10
w12=10
s=1*10+x1*10+x2*10
f(s) =
f(-4.6) ~ 0 & f(4.6) ~ 1
y=f(s)

## Slide 72: Learning: Neural Network
Learning  Adjusting Weights!
x1 | x2 | s | y=f(s) | Output
0 | 0 | -30 | 0 | 0
0 | 1 | -20 | 0 | 0
1 | 0 | -10 | 0 | 0
1 | 1 | -5 | 0 | 1
AND
x2
x1
+1
w01=-30
w11=20
w12=5
s=1*-30+x1*20+x2*5
f(s) =
f(-4.6) ~ 0 & f(4.6) ~ 1
y=f(s)

## Slide 73: Learning: Neural Network
Learning  Adjusting Weights!
x1 | x2 | s | y=f(s) | Output
0 | 0 | -30 | 0 | 0
0 | 1 | -10 | 0 | 0
1 | 0 | -10 | 0 | 0
1 | 1 | 10 | 1 | 1
AND
x2
x1
+1
w01=-30
w11=20
w12=20
s=1*-30+x1*20+x2*5
f(s) =
f(-4.6) ~ 0 & f(4.6) ~ 1
y=f(s)

## Slide 74: Learning Non-Linear Functions (MLP)
x2
x1
+1
30
y
20
20
x2
x1
+1
10
y
-20
-20
x2
x1
+1
-10
y
20
20
a
x2
x1
+1
30
20
20
b
10
-20
-20
-10
20
20
+1
x1 | x2 | a | b | Output
0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1
y
x1 & x2
~x1 & ~x2
x1 | x2

## Slide 75: Convolutional Neural Networks (CNN)
32x32x3
5x5x3
Convolution (Conv)

## Slide 76: Convolutional Neural Networks (CNN)
32x32x3
5x5x3
Convolution (Conv)

## Slide 77: Convolutional Neural Networks (CNN)
6
28
28
32x32x3
6 of 5x5x3
Convolution (Conv)

## Slide 78: Convolutional Neural Networks (CNN)
32x32x3
6 5x5x3
28x28x6
Convolution (Conv)
ReLU = max(0,x)
Pooling
Example of CNN = {Conv, ReLU, Pooling}, {Conv, ReLU, Pooling},…

## Slide 79: Datasets
The MNIST
  http://yann.lecun.com/exdb/mnist/
The CIFAR-10
  https://www.cs.toronto.edu/~kriz/cifar.html
The Street View House Numbers (SVHN)
  http://ufldl.stanford.edu/housenumbers/
ImageNet
  14,197,122 images
  http://image-net.org/

## Slide 80: Specific Examples of CNN Implementation

## Slide 81: CIFFAR Test Topology
32x32x3
32@3x3x3
32@32x3x3
32x32x32
32x16x16
64@32x3x3
64x16x16
64@64x3x3
128@64x3x3
128x8x8
128@128x3x3
32x32x32
64x16x16
64x8x8
128x4x4
128x8x8
pool
pool
pool
2048
1024
512
10

## Slide 82: Convolutional Net using CIFFAR: The first Layer
Convolution (Conv)
Input: 32x32x3
Filters: 32 of 3x3x3
Output shape: 32x32x32
32
32
32
32 of 3x3x3 filters

## Slide 83: CNN: Case Studies
LeCun, Yann, et al. “LeNet”
Alex, et al. “AlexNet”

## Slide 84: CNN: Case Studies
AlexNet requires 244 MB parameters 1.4. billion floating point operations per image
VGG-16 requires 552 MB of parameters and 30.8 GFLOP per image

## Slide 85: State-of-the-art

## Slide 86: DNN on an embedded systems
Inference
Training

## Slide 87: DNN on an embedded systems
Inference
Training
Hardware
Algorithm

## Slide 88: DNN on an embedded systems
Inference
Training
Hardware
Algorithm
Algorithm for Efficient
Inference
Hardware for Efficient
Inference
Algorithm for Efficient
Training
Hardware for Efficient
Training

## Slide 89: DNN on an embedded systems
Inference
Training
Hardware
Algorithm
Algorithm for Efficient
Inference
Hardware for Efficient
Inference
Algorithm for Efficient
Training
Hardware for Efficient
Training

## Slide 90: Algorithms for Efficient Inference
Quantization
Low Rank Approximation
Winograd Transform
Pruning + Weight Sharing  Deep Compression
Binary / Ternary Neural Network (BNN) (Extreme Quantization)

## Slide 91: Quantization
The main idea: Use smaller number of bit width
Suitable for embedded systems
Achieved 4.45 fps on embedded systems using low power
Qiu, Jiantao, et al. "Going deeper with embedded fpga platform for convolutional neural network." Proceedings of the 2016 ACM/SIGDA International Symposium on Field-Programmable Gate Arrays. ACM, 2016.

## Slide 92: Winograd Transformation
[1] Lavin, Andrew, and Scott Gray. "Fast algorithms for convolutional neural networks." CVPR2016.
[2] Aydonat, Utku, et al. "An OpenCL (TM) Deep Learning Accelerator on Arria 10." arXiv preprint arXiv:1701.03534 (2017).
Reducing the number of * operations when computing convolution

## Slide 93: Winograd Transformation
[1] Lavin, Andrew, and Scott Gray. "Fast algorithms for convolutional neural networks." CVPR2016.
[2] Aydonat, Utku, et al. "An OpenCL (TM) Deep Learning Accelerator on Arria 10." arXiv preprint arXiv:1701.03534 (2017).
Reducing the number of * operations when computing convolution
https://www.youtube.com/watch?v=E7QJUby9x-I
^ good explainer video

## Slide 94: Winograd Transformation
Implemented AlexNet on Aria FPGA 1150 (6.6 MB)
  Efficient data transfer between DRAM and FPGA
  Winograd Transformation
  Uses OpenCL
Results
  1020img/s on ImageNet
[1] Lavin, Andrew, and Scott Gray. "Fast algorithms for convolutional neural networks." CVPR2016.
[2] Aydonat, Utku, et al. "An OpenCL (TM) Deep Learning Accelerator on Arria 10." arXiv preprint arXiv:1701.03534 (2017).
https://www.altera.com/products/fpga/arria-series/arria-10/features.html

## Slide 95: Deep Compression
[1] S. Han, J. Pool, J. Tran, W.J. Dally, “Learning both Weights and Connections for Efficient Neural Networks”, NIPS’15
1) Pruning

## Slide 96: Deep Compression
[1] S. Han, J. Pool, J. Tran, W.J. Dally, “Learning both Weights and Connections for Efficient Neural Networks”, NIPS’15.
[2] S. Han, H. Mao, W. J. Dally, “Deep Compression: Compressing Deep Neural Networks with Pruning, Trained Quantization and Huffman Coding”, ICLR’16
[3] S. Han, X. Liu, H. Mao, J. Pu, A. Pedram, M. Horowitz, W. J. Dally, “EIE: Efficient Inference Engine on Compressed Deep Neural Network”, ISCA’16.
[4] F. Iandola, S. Han, M. Moskewicz, K. Ashraf, W. J. Dally, K. Keutzer, “SqueezeNet: AlexNet-Level Accuracy with 50x Fewer Parameters and < 0.5MB Model Size”, arXiv 16
1) Pruning
2) Weight Sharing

## Slide 97: Deep Compression

## Slide 98: Extremely Deep Compression
Using just 6% of the original network… better accuracy!
https://dl.acm.org/doi/pdf/10.1145/3131672.3131675
Using just 10% of the original network… better accuracy!

## Slide 99: 5) BinaryConnect & BinaryNet
Courbariaux, Matthieu, Yoshua Bengio, and Jean-Pierre David. "Binaryconnect: Training deep neural networks with binary weights during propagations." Advances in Neural Information Processing Systems. 2015.
Courbariaux, Matthieu, et al. "Binarized neural networks: Training deep neural networks with weights and activations constrained to+ 1 or-1." arXiv preprint arXiv:1602.02830 (2016).

## Slide 100: BinaryConnect: Binary Weights
Inference
Training
+1 / -1

## Slide 101: BinaryNet (Binarized Neural Network) BNN
BinaryNet
  Binary Input /Output Activations
  Binary Weights
)
In hardware, matrix multiplication  XNOR & Bitcount operations

## Slide 102: Binarized Neural Network
256-4096
256-4096
784
256-4096
Image
Conv3-64
Conv3-64
MP2
Conv3-128
Conv3-128
MP2
Conv3-256
Conv3-256
MP2
FC-512
FC-512
1. Binary Neural Network (MNIST)
2. Binary Convolutional Neural
Network (CIFAR)

## Slide 103: BinaryNet (BNN) Results
MNIST
  3 hidden units: 4096 neurons each + SVM,
CIFAR
  2x128@3x3 M2 2x256@3x3 M22x512@3x3 M2  2x1024 FC  10SVM
  No data augmentation or pre-processing
SVHN
  The same (half) of CIFAR
 | MNIST | CIFAR-10 | SVHN
Ordinary DNN | 1.30± 0.04% | 10.64% | 2.44%
BinaryConnect (D) | 1.29±0.08% | 9.90% | 2.30%
BinaryConnect (S) | 1.18±0.04% | 8.27% | 2.15%
BinaryNet | 0.96% | 11.4 | 2.8%

## Slide 104: CNV Topology: CIFAR & SVHN
32x32x3
64@3x3x3
64@64x3x3
32x32x64
16x16x64
128@3x3x64
16x16x128
32x32x64
pool
Image
Conv3-64
Conv3-64
MP2
Conv3-128
Conv3-128
MP2
Conv3-256
Conv3-256
MP2
FC-512
FC-512

## Slide 105: FINN Conclusion
Work |  | Accuracy | FPS /Latency
FINN | SFC (MNIST) | 95.83% | 12261 K (0.31 us)
FINN | LFC (MNIST) | 98.4% | 1561 K (2.44 us)
FINN | CNV (CIFAR-10) | 80.1%88% | 21.9 K (283 us)
FINN | CNV (SVHN) | 94.9% | 21.9 K (283 us)

## Slide 106: Can FPGA Beat GPUs in Accelerating DNN ?
1) Deep Compression
2) BNN

## Slide 107: DNN on an embedded systems
Inference
Training
Hardware
Algorithm
Algorithm for Efficient
Inference
Hardware for Efficient
Inference
Algorithm for Efficient
Training
Hardware for Efficient
Training

## Slide 108: DNN on an embedded systems
Inference
Training
Hardware
Algorithm
Algorithm for Efficient
Inference
Hardware for Efficient
Inference
Algorithm for Efficient
Training
Hardware for Efficient
Training

## Slide 109: Hardware for Efficient Inference
EIE
Diannao
Eyeriss
[1] Han, Song, et al. "EIE: efficient inference engine on compressed deep neural network." Proceedings of the 43rd International Symposium on Computer Architecture. IEEE Press, 2016.
[2] Chen, Tianshi, et al. "Diannao: A small-footprint high-throughput accelerator for ubiquitous machine-learning." ACM Sigplan Notices. Vol. 49. No. 4. ACM, 2014.
[3] Chen, Yu-Hsin, et al. "Eyeriss: An energy-efficient reconfigurable accelerator for deep convolutional neural networks." IEEE Journal of Solid-State Circuits (2016).
[4] DNPU: An 8.1TOPS/W Reconfigurable CNN-RNN Processor for General-Purpose DeepNeural Network
[5] Reagen, Brandon, et al. "Minerva: Enabling low-power, highly-accurate deep neural network accelerators." Proceedings of the 43rd International Symposium on Computer Architecture. IEEE Press, 2016.
DNPU
Minerva
Plethora of academic + industry

## Slide 110: DNN on an embedded systems
Inference
Training
Hardware
Algorithm
Algorithm for Efficient
Inference
Hardware for Efficient
Inference
Algorithm for Efficient
Training
Hardware for Efficient
Training

## Slide 111: Algorithm for Efficient Training
Batch Normalization
Model Distilation
DSD
[1] Ioffe, Sergey, and Christian Szegedy. "Batch normalization: Accelerating deep network training by reducing internal covariate shift." arXiv preprint arXiv:1502.03167 (2015).
[2] Romano, Nathanael, and Robin Schucker. "Distilling Knowledge to Specialist Networks for Clustered Classification.“
[3] S. Han, J. Pool, S. Narang, H. Mao, S. Tang, E. Elsen, B. Catanzaro, J. Tran, W. J. Dally, “DSD: Regularizing Deep Neural Networks with Dense-Sparse-Dense Training Flow”, ICLR’17.

## Slide 112: DNN on an embedded systems
Inference
Training
Hardware
Algorithm
Algorithm for Efficient
Inference
Hardware for Efficient
Inference
Algorithm for Efficient
Training
Hardware for Efficient
Training

## Slide 113: Hardware for Efficient Training
Hardware types
Specific hardware
Nvida Volta 100 with tensor cores
Facebook Big Sur (GPU based)
Distributed training on clusters

## Slide 114: 95% of the GPU version, and 89% on CPU is spent on convolutional layers
FPGAs are efficient platforms for convolution, BUT,…!
Jia, Yangqing. "Learning Semantic Image Representations at a Large Scale." (2014).

## Slide 115: References
GPU Teaching Kit
https://www.cs.unc.edu/~prins/Classes/633/Readings/CUDA_C_Programming_Guide_4.2.pdf
https://cseweb.ucsd.edu/classes/fa15/cse260-a/lectures.html